## Slide 1
Neurologic Diseases and Disorders, PTP 567
Dayna Ryan, PT, DPT
Winter 2012

## Slide 2
Shows the projected outlines and internal structures of the imaged object due to varying attentuation in the object
Normally take two projections at 90-degree orientations

## Slide 3
Advantages
  Inexpensive
  Readily available
  Good anatomic resolution of bones
Disadvantages
  Radiation exposure
  Poor differentiation of soft tissue structures

## Slide 4
Fractures
Ankylosing spondylitis
Structural anomalies
Arthritis
Tumors
Osteomyelitis

## Slide 5
The greater the density of tissue, the less penetration of x-rays (more white)
Low  High Density:
Air  Fat  Water  Soft Tissue  Bone  Metal

## Slide 6
Takes multi-angle images
Reconstructs a cross-sectional image using a computer
Examples
  CT Scan (uses x-ray images)
  SPECT (uses gamma ray images)
  PET (radioactive label with gamma ray images)

## Slide 7
Process of creating cross-sectional or tomographic images from projections of the object at multiple angles and using a computer for image reconstruction
CT scan uses x-ray images

## Slide 9
Advantages
  Excellent contrast resolution
  Excellent bony detail (get larger span on a gray scale compared to plain x-rays)
  Good soft-tissue structure resolution
  Compared to MRI, is quicker and more accessible to the unstable patient
  Easy to monitor patient
  Superior for detection of calcification and acute subarachnoid hemorrhage compared to MRI
Disadvantages
  Exposure to radiation is similar to plain x-rays
  Poor soft-tissue resolution in obese patients

## Slide 10
Disc protrusions
Facet disease
Spinal stenosis
Dislocations
Patellofemoral alignment
Osteomyelitis
Tumors
Hemorrhages, e.g. in brain with TBI or stroke
TBI: CT scan showing cerebral contusions with hemorrhage, subdural hematoma, and skull fractures
Notes: <number>

## Slide 11
Nuclear medicine = field of medicine which concerns the application of small doses of radioactivity for diagnostic purposes including laboratory tests, and larger doses for therapeutic purposes
Nuclear imaging = all procedures involving the detection of and image formation from the emissions of radiopharmaceuticals introduced into patients for diagnostic purposes
SPECT and PET are common procedures

## Slide 12
SPECT or SPET= single photon emission computed tomography
Tomographic nuclear imaging technique producing cross-sectional images from gamma ray emitting radiopharmaceuticals (single photon emitters or positron emitters)
Uses gamma ray cameras to take multiple images from different angles

## Slide 13
Advantages
  Can display images from one scan session in different planes
    Sagittal
    Coronal
    Horizontal
  Compared to planar images, has better contrast resolution
Disadvantages
  Compared to planar images, has inferior spatial resolution

## Slide 14
Bone scans (radionuclide bone imaging)
Distinguish between normal or pathologic processes in the spine
Differentiate between symptomatic and asymptomatic spondylolysis
Assess TMJ

## Slide 15
A low dose of a radiopharmaceutical labeled with a positron emitter such as C-11, N-13, O-15 or F-18 is injected into the patient, who is scanned by the tomographic system
Scanner detects the spatial and temporal distribution of the radiolabel by detecting gamma rays

## Slide 16
Disadvantages
  Expensive!
Advantages
  2-D and 3-D imaging is possible
  Shows metabolism of radiolabel
  Helps differentiate between scar tissue, necrotic tissue, active tumors, and normal brain tissue
  Less fuzzy than nuclear medicine with x-rays

## Slide 17
Location of epileptic seizure foci
Grading of brain tumors
Assessment of cerebral and cardiac perfusion
Assessment of cerebral function, metabolism and receptor ligand systems
Notes: <number>

## Slide 18
Production of an image using signal information from protons which have spin property
Notes: An MRI machine uses a powerful magnetic field to align the magnetization of some atomic nuclei in the body, and radio frequency fields to systematically alter the alignment of this magnetization. This causes the nuclei to produce a rotating magnetic field detectable by the scanner—and this information is recorded to construct an image of the scanned area of the body.[1]:36 Magnetic field gradients cause nuclei at different locations to rotate at different speeds. By using gradients in different directions 2D images or 3D volumes can be obtained in any arbitrary orientation.
<number>

## Slide 19
Advantages
  Greater ability to image the brain and spinal cord than other modalities such as CT
Disadvantages
  Not as quick to administer as a CT scan (important with unstable patients)
Brain metastasis in right hemisphere from lung cancer shown on T1-weighted MRI with contrast
Notes: <number>
ACL normal and ACL complete tear

## Slide 20
Sequences can be used to assess CSF flow and blood flow (magnetic resonance angiography)
Chemical composition of tissue can be obtained using magnetic resonance spectroscopy, (MRS)
Perfusion imaging is used to measure changes in blood flow in tissue (tracks hemoglobin)

## Slide 21
T1-weighted image:
  Cerebrospinal fluid (CSF) is black
  White matter is of higher signal (whiter) than grey matter (in a fully myelinated brain)
T2-weighted image:
  CSF is white
  White matter is lower in signal than grey matter

## Slide 22
T1 Weighted Image
T2 Weighted Image
T1 Weighted Image following Gadolinium Injection
Notes: <number>
Intradural extramedullary tumour, Fig. 2
MR, T1-weighted image. Isointense tumour, intradural extramedullary at the level of the conus medullaris, origin of the cauda. (remember that in T1 weighted images, CSF is black)
b. MR, T2-weighted image. The tumour has mixed signal, partially isointense and partially hyperintense. c. MR, (Remember that in T2 weighted images, CSF is white)
c. T1-weighted image following gadolinium injection. The tumour enhances almost homogeneously (meningioma).

## Slide 23
A noninvasive, diagnostic technique that records the electrical impulses produced by brain cell activity
The EEG uses special patches placed on the scalp or fine needles placed in the brain to record abnormal electrical currents inside the brain.

## Slide 25
Typically 16-20 electrodes placed on scalp
Invasive electrodes occasionally used
Continuous graphic recording of signal
Notes: <number>
Image:
Electroencephalogram. Recordings made while the subject was excited, relaxed, and in various stages of sleep. During excitement the brain waves are rapid and of small amplitude, whereas in sleep they are much slower and of greater amplitude.

## Slide 26
Sleep disorders
Stroke
Tumors
Encephalitis
Epilepsy
Degenerative diseases (i.e. Alzheimer's disease, Parkinson's disease)

## Slide 27
Awake adults: mostly alpha waves and beta waves
Symmetry between hemispheres
No abnormal bursts of electrical activity and no consistently slow brain waves detected

## Slide 28
Asymmetry between hemispheres
Sudden bursts of electrical activity (spikes) or sudden slowing of brain waves may indicate:
  brain tumor
  infection, injury
  stroke
  epilepsy if during a seizure
Delta waves or an excess of theta waves in adults who are awake may indicate:
  Brain injury
Notes: <number>

## Slide 30
Noninvasive tool to study epilepsy and brain function.
When combined with structural imaging, it is known as magnetic source imaging (MSI).
Measures small electrical currents arising inside the neurons of the brain. These currents produce small magnetic fields.
Generates remarkably accurate representation of the magnetic fields produced by the neurons.

## Slide 31
Similar to EEG (electroencephalography).
  difference is that the skull and the tissue surrounding the brain affect the magnetic fields measured by MEG much less than they affect the electrical impulses measured by EEG.
  advantage of MEG over EEG is therefore greater accuracy
  allows for more usable and reliable localization of brain function.

## Slide 32
Localization of seizures
  Combined with MRI and/or EEG to localize areas of seizure activity
Localizing electrical activity in normal brain function—not just structure!
More specific localization of brain tumors.
Takes about 1-2.5 hours.
http://abcnews.go.com/GMA/video/brain-scan-treat-seizures-9735607

## Slide 33
Purpose:
  Collect CSF -cerebrospinal fluid
  Reduce intracranial pressure in emergencies
Test CSF for:
  Meningitis
  Subarachnoid Hemorrhage