## Slide 1: Electromyogram (EMG) Defined
Electromyography (EMG) is an electrical recording of muscle activity which aids in the diagnosis of neuromuscular disease
Electrodes
  Needle
  Surface
Notes: Today’s talk is about diagnostic EMG for which needle EMG is used. Surface electrodes are used in the PT clinic as a non-invasive means of EMG examination or for use with biofeedback systems in treatment of various patient disorders.

## Slide 2: Electromygram (EMG) Procedure
Fine needle is inserted into the muscle to be tested.
Each muscle fiber that contracts will produce an action potential
Presence, size, and shape of the wave form of the action potential are recorded
Recordings are made while the muscle is at rest, and then during the contraction

## Slide 3: Electromyography (EMG) Parameters Recorded
Amplitude = negative peak to positive peak
Duration = time from first deflection of the baseline to the last return to baseline
Number of phases = number of times the components of the motor unit potential cross the baseline plus one
Rise time = elapsed time between the peak of the initial positive (down) deflection to the peak of the highest negative (up) deflection
Note: the number of fibers contained in a motor unit and their degree of synchrony affect these characteristics
Notes: Amplitude, duration, number of phases, rise time, and firing rates characterize a motor unit potential

## Slide 4: Electromyography (EMG) Insertional Activity
Insertional activity = response of the muscle fibers to needle electrode insertion
Normally consists of brief, transient muscle action potentials in the form of spikes, lasting only a few seconds and stopping immediately when needle movements stop
Abnormal insertional activity:
  Decreased
    Fibrosis
    Fat tissue replacement
  Increased
    Early denervation
    Myotonic disorders

## Slide 5: Electromyography (EMG) Spontaneous Activity
Persistence of any activity beyond insertion constitutes spontaneous activity
Could be due to the normal end-plate noise, or to the presence of fibrillations and positive waves, or other spontaneous activity
Normally, the monophasic potentials are of low amplitude and short duration and cause a "thickened baseline" appearance. They give a typical "sea shell" noise or "roar" on the loudspeaker.

## Slide 6: Electromyography (EMG) Pathology in Denervated Muscle
Fibrillations and Positive Sharp Waves occur with denervation because:
The acetylcholine receptors spread all across the muscle fiber instead of being grouped in the end-plate region
This spread may play a role in attracting new innervation to the denervated muscle fiber from adjacent nerve sprouts
The muscle fiber becomes much more sensitive to free acetylcholine released spontaneously from adjacent nerve fibers and is depolarized and repolarized spontaneously as these molecules reach it
Each single depolarization is electrically detected as a single muscle fiber action potential.

## Slide 7: Electromyography (EMG) Abnormal – Fribrillation Potential
Of short duration (<3 msec) and low amplitude (<300 µv), fibrillation potentials occur in semirhythmical runs (<30/second), though occasionally the frequency is so slow it appears to be random.
Develop two to three weeks after the neuron or axon has been damaged
Less frequently seen as time goes by and may be seen infrequently after three years.
As the muscle is reinnervated, both fibrillations and positive waves decrease in number and eventually disappear
Cannot be detected visually on the skin
Notes: At times, the fibrillations have been reported as long as twenty years after denervation, though they are typically less frequently seen after 3 years.

## Slide 8: Electromyography (EMG) Abnormal – Positive Sharp Wave
Very sharp positive deflection off the baseline followed by a slower return and often a negative phase before returning to the baseline
May reach up to 1 mv in amplitude and can last up to 50 msec
Discharge in a very rhythmic manner
Usually the rhythm starts and stops abruptly, and rarely does the individual rhythm vary

## Slide 9: Electromyography (EMG) Abnormal - Fasciculation
Spontaneous discharge of an entire unit in a random fashion
  Like a cramp
Looks like any motor unit, but is distinguished by the irregular discharge pattern
Can be detected visually on the skin
  Binine: regular, normal response
Notes: Fasciculation potentials can be monophasic or diphasic, looking like normal motor units, or highly polyphasic and complex, looking like neurogenic motor units.
The former, the so-called benign fasciculations, are usually seen in normal persons having fatigue or muscle cramps and usually occur at 0.8 second intervals. The latter, the so-called malignant fasciculations, are seen most frequently in anterior horn cell disease, though they have been observed with chronic neuropathies, radiculopathies, and Creutzfeldt-Jakob disease and tend to have longer intervals between each other, usually in the vicinity of 3.5 seconds.

## Slide 10: Electromyography (EMG) Repetitive Discharges
A.K.A. high frequency discharges and bizarre repetitive potentials
long trains of rapidly firing potentials with abrupt onset and termination
Seen in a variety of myopathic and neuropathic conditions.
  Polymyositis (Polio)
  early active stages of Duchenne muscular dystrophy
  chronic root lesions
  peripheral neuropathies
  motor neuron diseases
  nerve regeneration

## Slide 11: Electromyography (EMG) Myopathic Lesions
Result: unstable spread of the depolarizing current, causing considerable desynchronization in the motor units.
Typically these motor units are of low amplitude, short duration, and have a high number of phases.
In most myopathic lesions neurons remain intact while muscle fibers die or become diseased
This results in:
  reduced duration of the motor unit activation
  drop in its amplitude
Remaining muscle fibers will do one of the following:
  Atrophy
  Divide
  Separate into small fragments
  Split along their axes
Notes: On the loud speaker, they have a typical scratchy metallic sound that can be best compared to the noise of hail falling on a tin roof. Another characteristic of these motor units is their recruitment in very large numbers at fairly low voluntary effort. Indeed, with only a moderate degree of contraction, one can see a full interference pattern. This results partially from the little effort that each of these reduced size motor units can deliver, thus requiring large numbers of them to deliver an adequate effort.

## Slide 12: Electromyogram (EMG) Normal Response / Values
Muscle tissue is normally electrically silent at rest.
Once the insertion activity quiets down, there should be no action potential on the oscilloscope.
As voluntary contraction is increased, more and more muscle fibers produce action potentials until a disorderly group of action potentials of varying rates and amplitudes (complete recruitment and interference pattern) appears with full contraction.
Voluntary contraction will generate a characteristic biphasic response, i.e. a positive phase followed by a negative one
The rise time, strictly a function of the proximity of the needle tip to the muscle fibers of the contracting unit, is usually between 200 and 300 µsec.

## Slide 13: Electromyography (EMG) Primary Uses
Muscular dystrophy
Congenital myopathies
Mitochondrial myopathies-energy making parts
Metabolic myopathies
Myotonias
Peripheral neuropathies
Radiculopathies
Nerve lesions
Amyotrophic lateral sclerosis=Luegarics disease
Polio
Spinal muscular atrophy
Guillain-Barré syndrome
Ataxias
Myasthenias

## Slide 14: Nerve Conduction Velocity Studies (NCVs)
Performed to evaluate nerve function and localize site of involvement
Tests the velocity at which impulses travel through a nerve
Two types of NCVs
  Motor: stimulate nerve and record over muscle belly
    Proximal to distal
  Sensory: stimulate sensory nerve and record sensory nerve (not common motor-sensory nerve)
    Distal to Proximal
      Most are recorded orthodromically (in normal signal direction), though some are recorded antidromically (opposite normal signal direction)
Notes: O’Sullivan book states that NCVs are a type of EMG. I do not view them this way since they are distinctly a nerve test. They are, however, typically done at the same time that EMG studies are conducted.
Because both sensory and motor neurons exist in the same nerve, the only way you can differentiate motor and sensory nerve function is to pick up the motor nerve signal in the muscle rather than the nerve.

## Slide 15: Nerve Conduction Velocity Studies (NCVs)
Nerve is stimulated, usually with surface electrodes. One electrode stimulates the nerve with a very mild electrical impulse.
Resulting electrical activity is recorded by the other electrodes.
Distance between electrodes and the time it takes for electrical impulses to travel between electrodes are used to calculate the nerve conduction velocity.

## Slide 16: Nerve Conduction Velocity Studies (NCVs) Procedure
Evoked potentials may also be performed for additional diagnostic information.
NCVs are especially helpful when pain or sensory complaints are more prominent than weakness
Impulse given may feel like a mild electric shock.
  Pt. says it hurrts
To stimulate nerves deep to the skin you must use an insulated needle electrode with its uninsulated tip lodged near the nerve.

## Slide 17: Nerve Conduction Velocity Studies (NCVs) Motor Procedure
Procedure
  Supramaximal impulse is applied eliciting full contraction of muscles distal to stimulus
  Typically measured at two different locations and calculated together using equation
  M-wave = summated activity of all motor units in the muscle recorded
  Latency = time between stimulus and onset of M-wave

## Slide 18: Nerve Conduction Velocity Studies (NCVs) Motor Response
M-wave represents the summated activity of all motor units (some motor units will be recruited later than others due to slower conduction times), therefore amplitude and shape of wave are important
M-wave onset
Stimulus
Baseline
Notes: Latency just tells you how the fastest conducting fibers are working since the fastest conducting fibers initiate the M-wave. Therefore, need to look not only at the latency, but also the shape of the M-wave.
Proximal and distal M-wave shapes should be the same in a normal person.
If muscle is partially denervated, the M-wave amplitude will be decreased.

## Slide 19: Nerve Conduction Velocity Studies (NCVs) Normal Values: General Comments
NCV depends on:
  Diameter of nerve
    Larger =Faster (Sensory)
  Degree of myelination
Newborn infants have values that are approximately one-half that of adults, and adult values are normally reached by age 5
  Because haven’t finished myelination yet, periphery at age 5, CNS in teens
Significant decreases in NCVs after age 70
  Demyelination
Specific values available in tables
Notes: Have students explain why newborns and young children have slowed NCVs (peripheral nerves not fully myelinated).
For older adults there may be some damage to myelination which could be due to poor microcirculation around the nerve itself.

## Slide 20: Nerve Conduction Velocity Studies (NCVs) Normal Values
Motor Values
UE values
  Average is 60 m/s
  Range is 45-70 m/s
LE values
  Average is 50 m/s
Sensory Values
Typically between 45-75 m/s
Usually sharp wave, unlike rounded M-wave
Slightly faster than motor NCVs because of large diameter sensory nerves

## Slide 21: Nerve Conduction Velocity Studies (NCVs) Abnormal Values
Abnormal results may be from:
  Demyelination (destruction of the myelin sheath)
  Conduction block (the impulse is blocked somewhere along the nerve pathway)
  Axonopathy (damage to the nerve axon)
    Why we do test in 2 different places, to detect a more distal or proximal lesion.

## Slide 22: Nerve Conduction Velocity Studies (NCVs) Primary Uses
Alcoholic neuropathy
Diabetic neuropathy
Nerve effects of uremia (from kidney failure)
Traumatic injury to a nerve
Guillain-Barre syndrome
Diphtheria
Carpal tunnel syndrome
Brachial plexopathy
Charcot-Marie-Tooth disease (hereditary)
Chronic inflammatory polyneuropathy
Common peroneal nerve dysfunction
Distal median nerve dysfunction
Femoral nerve dysfunction

## Slide 23: H-Reflex Defined
= Hoffmann Reflex
The H Reflex results from stimulation of 1A afferent fibers with the resulting afferent discharge causing an excitatory potential in the motor neuron pool and muscle activation
Latency of response is a measure of integrity of both sensory and motor fibers
Notes: Stimulation of sensory fibers in nerve.
Recording from muscle contraction itself.

## Slide 24: H – Reflex Test of Sensory – Motor Reflex Loop
Notes: The H Reflex results from stimulation of 1A afferent fibers with the resulting afferent discharge causing an excitatory potential in the motor neuron pool and muscle activation

## Slide 25: H – Reflex Procedure
Submaximal stimulus applied to S1 nerve roots at tibial nerve in popliteal fossa
  Not pictured here
Motor response recorded in medial soleus
Sometimes done in C6-C7
  Pictured here

## Slide 26: H – Reflex Responses
NORMAL average response is 29.8 ms (+ 2.74 ms)
ABNORMAL responses
  Slowed latency  abnormal dorsal root function from herniated disk or impingement syndrome
    Peripheral motor and sensory NCVs are typically normal in this situation
    This test shows abnormalities before EMG denervation potentials would be present

## Slide 27: H – Reflex Primary Uses
Radiculopathy
Peripheral neuropathy

## Slide 28: F Wave Defined
A measure of motor neuron conduction
Supramaximal stimulus of motor neurons at a distal site leading to both orthodromic (get distal muscle contraction) and antidromic impulses (goes to anterior horn cell  reverberates there  impulse sent back down motor neuron  recorded)
Antidromic portion of response is response that is called the F wave
Notes: Not considered a reflex since there are no synapses involved.

## Slide 29: F Wave Normal Values (Latencies)
Upper Extremity
  Approximately 30 seconds
Lower Extremity
  Less than 60 seconds

## Slide 30: F Wave Primary Uses
Conditions where proximal nerve is involved
Guillain-Barre Syndrome
Thoracic Outlet Syndrome: UE
Brachial Plexus injuries
Radiculopathies with more than one nerve root involved
As measure of alpha motor neuron excitability in research studies

## Slide 31: Ultrasound Defined
Propagated sound waves interact with tissue interfaces to produce images based on reflection or refraction of structures with different acoustic impedance
  For Deep Vein Thrombosis
Sound waves are reflected back to a transducer crystal and converted into electrical input
Doppler ultrasound technique produces color-coded real-time images of blood flow.

## Slide 32: Ultrasound Advantages / Disadvantages
Advantages
  noninvasive
  relatively low cost
  Safe, with no radiation
  Quick
  allows localization of lesions in three dimensions, therefore useful for guiding percutaneous aspiration or biopsy and for mapping radiation portals
Disadvantages

## Slide 33: Ultrasound Primary Uses
Superficial tendons and muscles
Popliteal space
Patellar tendon
Many joints
Popliteal cysts
Tumors and infections of bone and soft tissue
Foreign bodies
Parathyroid glands
Hematomas
Notes: Power Doppler image (upper) shows cortical perfusion in right kidney; color Doppler (lower) shows only the larger vessels

## Slide 34: Echocardiography
Cardiac imaging technique based upon the velocity of sound traveling through and reflected from acoustic interfaces in cardiovascular structures
Most frequently performed diagnostic study for cardiac diseases
2-D format most typically used
Doppler format used to examine blood flow through the heart
  Transthoracic typically performed
  Transesophageal echocardiography involves placement of the ultrasound transducer into the esophagus in proximity to the heart and is sometimes done during cardiac surgeries

## Slide 35: Echocardiography Advantages / Disadvantages
Advantages
  Non-invasive (other than the transesophegeal form)
  Readily available
Notes: Image:
Transesophageal echocardiogram in the four chambers view demonstrates a myxoma (MYX) attached to the atrial septum. LA = left atrium; LV = left ventricle; RA = right atrium; RV = right ventricle. Reproduced from Himelman RB: Echocardiography in Acquired Heart Disease. In: Higgins CB: Essentials of Cardiac Radiology and Imaging. JB Lippincott, Co., Phila., PA, 1992.

## Slide 36: Echocardiography Primary Uses
Blood flow mapping of the heart and its blood vessels
Transesophageal echocardiography
  imaging of the heart during and after cardiac surgery in the operating room
Stress echocardiography involves the evaluation of regional wall motion following a pharmaceutical stress

## Slide 37: Arthrography
Contrast opacification of joint cavities which are then recorded by fluoroscopy, CT, or digital radiography
Application of stress is useful in arthrographic evaluation of ligamentous injuries of the ankle, wrist and first metacarpophalangeal joint.
Notes: Arthrography typically used before MRI for ACL type injuries.
Intra-articular injection of a positive contrast medium. Then an x-ray is taken.

## Slide 38: Arthrography Advantages / Disadvantages
Advantages
  Can apply stress to a joint during imaging
  Good soft tissue images
Disadvantages
  Need to inject a radio-opaque substance into joint
Notes: Image:
AP radiograph of the shoulder after intra-articular injection of contrast material demonstrates a full thickness tear of the rotator cuff (arrow) and resultant extravasation of contrast material into the subacromial subdeltoid bursa.

## Slide 39: Arthography Primary Uses
Wrist
Elbow
Glenohumeral
  rotator cuff tears
  adhesive capsulitis
  bicipital tendon abnormalities
  rheumatoid arthritis
  septic arthritis
Hip
  developmental dysplasia
  septic arthritis in infants,
  Legg Calvè Perthes disease
  traumatic injuries
  soft tissue masses
Knee (rarely done now since advent of MRI)
Ankle

## Slide 40: Bone Scan
Produced using radiopharmaceutical agents
Shows metabolism of bone
Increased uptake of the radionuclide agent at sites of bone abnormalities
Typically imaged with single photon emission computed tomography (SPECT)
May be imaged with PET scan

## Slide 41: Bone Scan Advantages / Disadvantages
Advantages
  Very sensitive
Disadvantages
  Not specific since any process involving changes in bone production and resorption can cause abnormalities on bone scans

## Slide 42: Bone Scan Primary Uses
Bone metastases
Osteomyelitis
Ischemic necrosis of bone
Differentiating osteomyelitis from cellulitis
Notes: Image on this slide:
Coronal whole-body FDG-PET scan (thickness 7 mm) of a patient showing normal FDG accumulation in the brain and the renal excretory system as well as a pathological focal accumulation medial to the right tibia due to metastasis of malignant melanoma.

## Slide 43: References
Gale Encyclopedia of Medicine
http://www.nlm.nih.gov/medlineplus/ency
Dorland’s Medical Dictionary
http://www.teleemg.com/Chapters/jbr110.htm
http://www.hucmlrc.howard.edu/neuroanat/Lectures/funanatspincrd.htm