## Slide 1: Medical Imaging in Musculoskeletal Diseases and Disorders
PTP 565, 2012

## Slide 2: Objectives
Introduce Other Medical Imaging Studies
  Digital Radiology, Tomography, CT scans, Fluoroscopy
  MRI Imaging
  US Imaging
Develop an understanding of the physics behind these imaging studies
List pro’s and con’s of each imaging technique
Compare and contrast imaging techniques

## Slide 3
http://www.med-ed.virginia.edu/courses/rad/ext/index.html
Great URL to test your knowledge of anatomy using radiology

## Slide 4: Radiographic Images Definitions:
Computed Radiograph (CR):
  Similar to a traditional radiograph but utilizes a different processing technique involving a phospho imaging plate.
Digitized Radiograph (DR)
  Does not use a processing agent such as silver (plain film) or phosphorous (CR), utilizes only a digital receptor to record the image

## Slide 5: Definitions:
Tomography
  X-ray tube and film move about a fulcrum, conventional or computed processing technique is used and only a specific plane or slice of the body is in focus. All else on the image is blurred.
Computed Tomography (CT)
  Combines multiple x-rays with computing power to create a tomographic image of a body slice. Axial slice of the body.
Fluoroscopy
  Dynamic or continuous radiograph exam. Real time imaging of movement, a video, allows active diagnosis during the film.

## Slide 6: Computed Radiography (CR)
Computed imaging:
Different processing technique than plain film radiographs.
x-ray beam projects an image onto a photostimuable phosphor imaging plate
www.medimagesys.com/

## Slide 7
Imaging plate stores the radiation level (electrons) received after the x-ray beam is opened.
The plate is then put through a scanner.
Scanner has a laser beam which causes the electrons to emit a light detected by the photo-multiplier tube and converts it to an electronic signal.
www.sprawls.org/resources/DIGRAD/module.htm
Remove frame

## Slide 8
Electronic signal is converted to a digital value which is then processed in an image processor pixel map.
Imaging plates can be reused over and over again if handled well.
www.sprawls.org/resources/DIGRAD/module.htm
Remove frame

## Slide 9: Advantage:
  Less expensive
  No silver based film or chemicals are required to process film
  Can be converted into a digital image and stored easier than plain film
  Imaging plate is environmentally safer than plain film
  Faster image acquisition
  Can adjust exposures, requiring less retakes

## Slide 10: Disadvantages
  Cassette requires handling
  Can erase an image if exposed to fluorescent light
  Imaging plates are very expensive
  Film quality issues with problems of geometric sharpness being less than conventional radiographs
  Lower spatial resolution compared to conventional radiographs

## Slide 11: Digital Radiography
Digitized Radiograph (DR)
  Does not use a processing agent such as silver (plain film) or phosphorous (CR), utilizes only a digital receptor to record the image
www.sprawls.org/resources/DIGRAD/module.htm

## Slide 12: Digital Radiography Equipment
  A digital image receptor: device that intercepts the x-ray beam after it has passed through the patients body and produces an image in digital form, that is, a matrix of pixels, each with a numerical value.
    Replaces the film cassette that is used in plain film radiography
www.sprawls.org/resources/DIGRAD/module.htm

## Slide 13
  A digital image processing unit
Uses an image reader with a laser scanner to reproduce the image

## Slide 14
  An image management system
    Image management is a function performed by the computer system associated with the digital radiography process.
    These functions consist of controlling the movement of the images among the other components and associating other data and information with the images.

## Slide 15
Image and data storage devices
  Digital radiographs, and other digital medical images, are stored as digital data.
  Advantages (compared to images recorded on film) include:
    Rapid storage and retrieval
    Less physical storage space required
    Ability to copy and duplicate without loss of image quality.

## Slide 16
  Interface to a patient information system
    One of the major advantages of digital radiography is the ability to process the images after they are recorded.
    Various forms of digital processing can be used to change the characteristics of the digital images.

## Slide 17
  A communications network
    Another advantage of digital images is the ability to transfer them from one location to another very rapidly.
    This can be:
      Within the imaging facility to the storage and display devices
      To other locations (Teleradiology)
      Anywhere in the world (by means of the internet)

## Slide 18
  A display device with viewer operated controls
  Major advantage: ability of the viewer to adjust and optimize image characteristics such as contrast.
  Other advantages include the ability to zoom, compare multiple images, and perform a variety of analytical functions while viewing the images.

## Slide 19: Advantages:
Can manipulate acquired image to produce alternative images
Manipulation of contrast and brightness can occur
Spatial resolution can be maximized
Number of increments for shading between black and white is greater so finer differences can be noted
Use a subtraction technique to remove structures and isolate tissue

## Slide 20: Disadvantages:
Can, potentially expose a patient to more x-ray beam radiation than necessary
Not as affordable as a CR system, higher costs because the existing systems (CR or plain film) will need to be replaced
Portable units are too expensive to be widely used

## Slide 21
Check the outline detail on the digital radiograph of the hand
Arrow points to a piece of glass embedded in the tissue

## Slide 22: Tomography
Tomography
  X-ray tube and film move about a fulcrum.
  Conventional or computed processing technique is used
  Only a specific plane or slice of the body is in focus.
  All else on the image is blurred.

## Slide 23: Tomograph Simpliefied
X – Ray Beam
Film Cassette
Xray Beam is moving to the right, film cassette is moving to the left. At present, all images
Are blurred due to the motion.

## Slide 24
When the film and the x-ray beam move into alignment with each other, a focused
Image can be taken. All surrounding tissue is blurred giving clear detail to that image

## Slide 25: Advantages
Can see fractures of irregular shaped bones more clearly
  Tibial plateau
  Cervical spine
If a fracture has a plate or screws, can image under this to determine bone healing
http://www.mikrondigital.com/index.php?page=tomosynthesis

## Slide 26: Disadvantages
Poor soft tissue detail
High radiation doses
Difficult to get exact plane/image especially in trauma patients
Tomography by itself has been replaced by Computed Tomography (CT) or Magnetic Resonance Imaging (MRI)

## Slide 27: Computerized Tomography
Process of creating cross-sectional (tomographic) images from projections of the object at multiple angles
Uses a computer for image reconstruction
www.rrvr.net

## Slide 28: Computed Tomography (CT)
CT scan uses x-ray images to analyze shape, symmetry, position and density of body structures
Examples
  CT Scan (uses x-ray images)
  SPECT (uses gamma ray images)
  PET (radioactive label with gamma ray images)

## Slide 29: CT SCAN
1. Slice of body, many angles, x-ray revolves around body
2. Detectors record
3. Computer compares views and makes one image
National Geographic, 1987

## Slide 30: Spiral CT
As patient moves through the scanner, the x-ray rotates continuously
Multi slice or multidimensional scanner

## Slide 31: CT Scan
Uses a higher radiation dose
Evaluates musculoskeletal trauma particularly in spine, acetabulum, glenoid, tibial plataue
Able to pick up metabolic bone diseases, tumor and congenital abnormalities well

## Slide 32: Computed Tomography (CT): Best in Imaging:
Bone and soft tissue tumors
Excellent at evaluating subtle or complex fractures
Intra-articular abnormalities such as loose bodies within a joint
Degenerative changes of bone
Detection of small bone fragments
Quantitative bone mineral analysis
☺First imaging choice with serious trauma as it can view both bone and soft tissue injuries
Spinal stenosis
Less time consuming than an MRI or an Ultrasound
More cost effective than an MRI
Works well for patients who are claustrophobic

## Slide 33: Limitations of CT
Average volume effect: computer applying average values to small volume of tissue and displaying it in one shade of gray even though it contains more than one type of tissue.
Doesn’t differentiate the histological make up of the tissue
Exposure to radiation is similar to plain x-rays
More valuable in thinner patients than in more obese patients

## Slide 34: CT images
In soft copy or digital format
Allows for manipulation of the contrast and density scales to get better pictures of the anatomy and pathology
Types of manipulation
  MPR
  MIP
  SSD
  VR
  And combinations of the above

## Slide 35: MPR:
MultiPlannar Reformatted image of a tibial plateau fracture

## Slide 36: MIP
Maximum Intensity Projection
  Vascular applications
  MR angiography or MRA commonly uses this technique
www.cg.tuwien.ac.at/research/vis/vismed/NPVR/

## Slide 37: SSD
Shaded Surface Display
  Helps to give a three dimensional view of the surface of a structure
  Used in orthopedic and vascular imaging studies
http://www.healthcare.philips.com/pwc_hc/main/shared/Assets
/Images/CT/Visualization_software/oa_3d_ssd_02_en.jpg

## Slide 38: VR
Volume Rendering
  Method combines the characteristics of the SSD and MIP.
  Allows color coding of tissues thus visual differentiation.
  3D method of choice as it is quickly able to process these pictures
www.cg.tuwien.ac.at/research/vis/vismed/NPVR/

## Slide 39
A: sagittal axial slice
B and C: SSD 3D images
D: MIP
E: MPVR – multiplanner volume
rendering
Aortic aneurysm
www.biomedcentral.com/1471-2342/2/1/figure/F3?highres=y

## Slide 40: Fluoroscopy
In use since the early 1990’s
Used as an anatomical guide utilized during minimally invasive and microscopic surgical procedures
Used with many types of diagnostic tests (e.g. discography).
www.spineuniverse.com/exams-tests/fluoroscopy

## Slide 41: Components
X-ray tube
Image intensifier unit
Fluoroscopic carriage
www.medtek.ki.se/medicaldevices/album/Ch%207%...

## Slide 42
http://www.youtube.com/watch?v=MMZCAaeQB_c
Advantages:
  Patient is moving
  Cost
Disadvantages:
  Radiation

## Slide 43: Magnetic Resonance Imaging Defined
MRI: A medical imaging technique which is based on the re-emission of an absorbed radio frequency while the patient is within a strong magnetic field.
MRI involves an interaction between a magnetic field and the nuclei of atoms

## Slide 44: Equipment
Scanner
  Magnet
  Gradient coils
  RF coils
Computer
National Geographic 1987

## Slide 45: Gradients
Gives the ability to create an image in any orientation – axial, coronal, sagittal
This occurs with the gradient coils
By convention, the external magnetic field is in the z direction
Gradient coils are either x or y direction
Gradient coil
http://www.berlin.ptb.de/en
/org/8/81/Laboratories/3T_
MRI.html

## Slide 46: How it works:
Atom consists of a neutron (neutral) and proton (positive) surrounded by orbiting electrons (negative).
Electrons rotate around the nucleus and around their own axis as well.
Neutrons and protons also spin about their own axes and possess nuclear spin.
http://upload.wikimedia.org/wikibooks/en/5/5d/SpinningProtonMagnet.gif
Nuclear spin is essential for
creating a MRI image

## Slide 47
Hydrogen is principle element used with an MRI
Hydrogen nucleus has a single proton
Spinning nucleus is a magnet which is affected by the external magnetic field of a MRI.
All the protons line up either parallel (spin up) or longitudinal magnetization or anti-parallel (spin down) or transverse magnetization to the magnetic field

## Slide 48: Alignment
Initially, proton’s line up parallel to the magnetic field
RF or a radiofrequency pulse is emitted sending the proton’s out of alignment
Once the RF is no longer emitted, the proton’s realign
Proton’s release the energy they absorbed as they realign
This release of energy causes a current to occur in the receiver coil of the MRI which gives information utilized for a MRI study

## Slide 49: T1 and T2 images
Contrast in an MRI image comes from T1 and T2
Taken at the same time, but are different processes
T1 and T2 complement each other
Following the RF Pulse
  Protons gain longitudinal magnetization – realign with the magnetic field
  Protons lose their transverse magnetization

## Slide 50: Image creation
MRI will utilize the differences of T1, T2 and proton density (number of hydrogen nuclei within the different tissues)
Different sequences target these differences
Sequence: image protocol characterized by timing of events during image acquisition

## Slide 51
Difference between T1 and T2 imaging is in the different TE and TR values.
TE: time at which the signal is captured
  Also called time to echo
TR: time at which the RF is repeated which displaces the protons again
  Also called time to repetition

## Slide 52: T1 Image
Short TR and TE times
Signal is caught early
Time is optimal to catch the differences between fat and water
Tissues that rapidly recover the longitudinal magnetization will have a higher signal intensity
Fat: bright image
Tissues which are high free water content, have low signal intensity with short TE times. Image darker

## Slide 53: T1
Use the ABCDS search strategy
Darker the color, the more the water content
Spinal cord has a darker outline around it from the CSF
Cauda equina can be seen
T1: used to identify anatomy
http://www.mr-tip.com/serv1.php?type=img&img=Anatomic
%20Imaging%20of%20the%20Lumbar%20Spine

## Slide 54: T2
Long TR and TE times
Signal is measured late in decay process
Tissues that are reluctant to give up energy image brighter
Water is slow to give up energy so has high or bright signal
Fat gives up energy quickly, low intensity, darker color
H20
  2 in H20 and T2,
  Water (H20) bright T2

## Slide 55: T2
Notice the CSF as being a very bright white in color
Intervertebral disc nucleus (whiter) is surrounded by the annulus (darker)
Spinal cord is darker in color
Used to identify pathology
http://www.mr-tip.com/serv1.php?type=img&img=Anatomic
%20Imaging%20of%20the%20Lumbar%20Spine

## Slide 56: Compare and Contrast T1 and T2 images
T1
  Fat appears white
  Water appears gray
  Bone marrow appears bright
  Bone cortex appears dark
  Good to review the anatomy
T2
  Fat appears gray
  Water appears white
  Bone marrow appears gray
  Bone cortex appears dark
  Good for pathology such as inflammation as it is usually water based.

## Slide 57: MR Image Enhancement
IV injection of Gd-DTPA or gadolinium will increase the signal intensity on a T1 weighted image.
Not the same as contrast enhancement in the way it occurs but accomplishes the same task.
Shortens the T1 and T2 relaxation times resulting in an increase in signal intensity on T1 weighted imaging sequences.

## Slide 58
Arrow points to a mass within the dural sac below the cauda equina
The structure imaged much whiter with the Gd-DTPA given intravenously
T1 T1 with Gd-DTPA
www.ispub.com/journal/the_internet_journal_of...

## Slide 59: Proton Density Image
Number of Hydrogen nuceli present, per unit volume, in a tissue to create a signal.
This quantity is the PRINCIPLE method of tissue differentiation
Use a long TR permitting full recovery of both fat and water
Uses a short TE in which neither fat nor water have much time to decay

## Slide 60
Tissues with a high density of protons give rise to a higher signal intensity
Low water-content areas such as bone or lung, have a low Signal Intensity
Similar to T1images, better anatomical detail
www.thecni.org/reviews/12-1-p13-dungan.htm

## Slide 61: Spin-Echo Pulse Sequence
RF pulse sequence which begins with a 90 dg excitation pulse followed by a 180 dg re-phasing pulse
First pulse (90 dg) tips the net magnetization into the transverse plane.
When the 180 dg pulse is emitted, a spin echo is obtained.

## Slide 62: T1 Fast Spin Echo
T1 image: fluid will image darkest
This is a slice of the femur and tibia. In this slice, the fibular head is just starting to appear at the lateral aspect of the knee
http://www.gehealthcare.com/euen/mri/
products/signa-ovation-035t/image-gallery/ortho.html

## Slide 63: STIR
Short Tau Inversion Recovery Image
TR is long
TE is short, slightly longer though than T1or PD
Images are similar to T2, emphasis on tissues that have a lot of fluid
Poor resolution
http://www.learningradiology.com/archives06/COW%20220-Osteochondritis%20dissecans/osteochondritisccorrect.html
T1 image
STIR image

## Slide 64: MRI Search Strategies
Organize into sequence groups: T1, T2, PD, STIR etc.
Arrange film sheets from each sequence into plane of view
  Axial
  Sagittal
  Coronal
Each film sequence contains slices from 4-8 mm thick.
Identify by scout film the first film in each sequence
Anatomical view
  Patient facing you in coronal studies
  Vertically in sagittal studies
  From supine through feet to head

## Slide 65
Scout film
www.nzma.org.nz/journal/119-1236/2032/
Notes: Feet to head, inferior to superior.

## Slide 66: Magnetic Resonance Imaging (MRI) Advantages /Disadvantages
Advantages
  No Radiation
  Greater ability to image the brain and spinal cord than other modalities such as CT
  Soft tissue evaluation of brain and body superior
  Others?
Disadvantages
  Not as quick to administer as a CT scan which is important with unstable patients
  Claustrophobia
  Any ferrous metal can be displaced within an MRI field
  Contraindicated with pacemakers, fusion, screws, tattotes.

## Slide 67: Ultrasound: Definition
Sound with a frequency greater than 20,000 Hz
Ultrasound Imaging (USI) uses sound waves within 3.5 to 15 MHz.
Diagnostic USI: examines the effect of injury or disease on muscles, ligaments, tendon
  Looks at muscles work.
Rehabilitative USI: evaluates muscle structure and behavior and uses USI as a biofeedback mechanism

## Slide 68: How Ultrasound works
Transducer collects reflected sound waves (echoes) and converts them back into electrical signals
  Piezoelectric effect
These signals are then converted to a digital image
Echoes return to transducer, are processed and displayed as pixels
The brightness of the pixel depends upon the echo strength which is determined by the location and specific characteristics of the echo-generating structure

## Slide 69
Orientation to an ultrasound image
Top to Bottom is depth
Darker lines are certain anatomy to examine.
The transducer is at the top and the sound waves radiate downwards
www.sprawls.org/ppmi2/USPRO/

## Slide 70
Frequency: number of oscillations that a wave undergoes in one second. Expressed in Hz
  1 Hertz (Hz) = 1 oscillation/second
  1 kilohertz (kHz) = 1000 oscillations/second
  1 megahertz (MHz) = 1 million oscillations/second
The higher the frequency of sound, the less the wave will diverge. This makes the waves very cohesive and able to focus on a specific target
Most common frequencies: 3.5-10 MHz
Notes: Higher frequency sends a better picture.

## Slide 71
Speed at which ultrasound travels is determined by the compressibility (molecular structure) or hardness of the medium it is traveling in.
The more rigid or hard the material, the faster the sound wave travels through it.
Average speed through soft tissue is 1540 meters/second
Velocity through water 1485-1526 m/s
Ultrasounds are calibrated to assume that sound travels through all tissue at 1540m/s

## Slide 72: Basic Principle: Attenuation
Ultrasound enters the body, propagates and encounters tissues of different density (interfaces).
Each tissue has a natural resistance to sound (acoustic impedance)
Value of acoustic impedance is dependent upon the density of the medium and the speed at which sound can travel through it.
At each interface, sound wave reacts and loses energy.
Notes: Bone=white, Empty space=black, under bone will be black.
As it goes down it will lose some energy and speed.
Attenuation is what happens to the sound waves when it hits the tissue whether it scatters, gets absorbed, or bounces back.

## Slide 73
Energy within a sound wave decreases as it penetrates until completely dispersed.
Attenuation is the result of reflection, scattering and absorption.
  Sound waves hit a tissue interface, the sound wave breaks up or fractures
    Fractured portion deflected: Scattering or Reflection
    Energy transferred to surrounding tissue as heat: absorption
    80% of sound wave is absorbed, rest is scattered or reflected

## Slide 74
Attenuation limits penetration of the sound wave and the depth of the image that can be generated.
Attenuation and frequency are directly related
The higher the frequency, the greater the attenuation and the more shallow its penetration.
The greater the attenuation, the more echo (reflection) is created and the better the resolution of the ultrasound image

## Slide 75
Frequency choice used for imaging is dependent upon the depth of the region or structures that will be imaged.
Higher frequencies: more superficial the structure (superficial muscles)
Lower frequencies: more depth of the structure (abdominal cavity)
General Rule: highest frequency transducer that can image an area of interest should be used.
Whittaker J. pg. 4
Notes: Depth=lower frequency
Shallow=higher frequency

## Slide 76: Basic Principle: Reflection
Reflection of sound waves produces the pattern of echoes that are then generated into a picture
Pattern is dependent on:
  The size of the reflecting medium
  Roughness of its surface
  Incident angle of the sound wave when it encounters the medium is important, want 90 degree angle.
  Difference in impedance of the two media that create the interface

## Slide 77
More irregular the surface, the greater the difference in impedance
More perpendicular a sound wave encounters the interface, the greater the proportion of the deflection that will be reflected back to the transducer versus that which is lost to scattering or absorption.

## Slide 78
Impedance of medium = density multiplied by speed at which the ultrasound can propagate through it.
Impedance increases if either density or propagation speed of the medium increase
Greater the impedance between two media, the greater the intensity of the echo generated at the interface, the brighter (whiter) the interface appears on the digital image.
No impedance, no echo, nothing is seen on the image

## Slide 79: Bone:
Great density, great attenuation (absorbs or reflects) back 100% of the sound that reaches it.
Bone produces a substantial reflection, surface appears bright white
Bone prevents transmission of sound to structures that are deep to, distal, or on the other side of it.
Area distal to the bone will appear black
Notes: Pic: cortical bone=bright white, fascia=whiter tissue, gray between is muscle

## Slide 80: Muscle:
Varies dependent on its orientation, architecture, morphology and anatomical location.
Healthy muscle has large amounts of blood
Fascia around it is less vascular, quite dense
Muscle layers are darker with shades of gray and fascia will appear much whiter.
Muscle with fatty infiltration appears whiter as it has greater echogenicity (atrophy of muscle)

## Slide 81: Fluid: blood or urine
Provides little impedance to sound waves
Causes minimal attenuation
Transmits sound waves well
Hypoechoic, appears black on ultrasound image
Transmit sound to structures that lie deep to I
Acoustic window to deeper structures
  EX: using a full bladder to view the pelvic floor

## Slide 82: Gas, subcutaneous fat, muscle-fat combinations:
Decrease clarity of the ultrasound image
Scattering effect on the ultrasound wave
Cause imaging and interpretation issues and difficulty in visualizing deeper structures.
A heavier person will be harder to image using ultrasound on the deeper structures than a thinner person

## Slide 83: Artifact:
Anything that is an incorrect representation of the anatomy
Produced by:
  Improper equipment operation
  Imaging technique
  Physics of ultrasound
Structures are not real, missing, improperly located or improper brightness, shape or size
Up to 16 different types, shadowing and enhancement have greatest impact for therapists/readers

## Slide 84: Instrumentation
For Physical Therapists, the portable diagnostic ultrasound makes the most sense.
In particular, to use this in practice for real time viewing of muscle action requires this portability.
For consideration of purchase, contact reps and ask to try in clinic for a period of time. See which one would be best for you.

## Slide 85: Medical Ultrasound Imaging Systems
4 generic components
  1. Beam former: generates the electrical impulses that drive the transducer
    Amplifies and digitizes the electrical signal returning from the transducer
  2. Signal processor: filters the signal and compresses it and sends it to the image processor
  3. Image processor: converts the digitized, filtered and compressed echo data into visual images
  4. Display: shows the visual images

## Slide 86: Transducers: Whittaker J. pg15
Notes: Curve=deeper=abdominal, multifidia

## Slide 87: Do Not Know for Exam
Brightness Mode USI
    B Mode
Ultrasound echo displayed as a cross-sectional grey-scale image
Typically associated with ultrasound imaging
Large viewing field
Real-time nature of USI
Can see several structures at once and over time
Depicts shape, size, composition and resting state of a structure (muscle, nerve etc.)
Motion, movement Mode
  M Mode
M-mode displays information collected from the midpoint of the transducer as a continuous image over time
Time is on x-axis, depth on the y-axis; m-mode represents the changes in thickness or depth of a structure over time.
Time-motion mode
Reliable measurement of muscle thickness

## Slide 88: Diagnostic Ultrasound
Great link to a UM website that shows the ultrasound images of normal and pathological soft tissue for the peripheral joints.
http://www.med.umich.edu/rad/muscskel/mskus/index.html
Musculoskeletal Ultrasound by J. Lin and W. Weadock

## Slide 89: Diagnostic Ultrasound
Musculoskeletal
  Images ligaments, tendon, nerve, muscle, tumors and foreign bodies
  Sensitivity and Specificity can equal MRI
    Rotator Cuff Tears 93% sensitivity, 94% specific
    ( Deyle, G. Evidenced Based Principles of Musculoskeletal Imaging, 3/2009 course notes.)

## Slide 90: Rehabilitative Ultrasound Imaging (RUSI)
A procedure used by physical therapists to evaluate muscle and related soft tissue morphology and function during exercise and physical tasks.
It is used to assist in the application of the therapeutic interventions aimed at improving neuromuscular function.
  - Teyhen DS. Rehabilitative Ultrasound Symposium San Antonio TX, 2006.

## Slide 91: RUSI
Used to help understand the relationship between motor control and function
Determine which patients benefit from a specific treatment approach
Enhance treatment efficacy via biofeedback
Document benefits of specific exercise programs

## Slide 92: Scope of Physical Therapy Practice
USI by a clinician is dictated by their profession and its scope of practice.
In physical therapy, this is the individual state practice acts. Check your state practice act. Can you do Diagnostic USI or RUSI?
Michigan Practice Act:
“Physical measures include massage, mobilization, heat, cold, air, light, water, electricity, and sound. Practice of physical therapy does not include the identification of underlying medical problems or etiologies, establishment of medical diagnoses, or the prescribing of treatment. “Section 333.17801
Therefore, in MI, I assume I can do RUSI

## Slide 93: References
Biederman R. Fundamentals of Musculoskeletal Imaging: MRI Interpretation in Physical Therapy Practice – Part II. 2006:1-12. LaCrosse, Wis: Orthopaedic Section, APTA, Inc.
Deyle GD. Evidence-Based Principles of Musculoskeletal Imaging. Course Notes. March 2009. Wyandotte, MI.
Greenspan A. Orthopedic Imaging, A Practical Approach, 4th ed. Lippincott, Williams and Wilkens, Philadelphia. 2004
McKinnis L. Fundamentals of Musculoskeletal Imaging, 3rd ed. F.A. Davis, Philadelphia. 2005
Malone TR, Hazle C, Grey ML. Imaging in Rehabilitation. McGraw Hill, 2008. New York.
Swain J, Bush K. Diagnostic Imaging for Physical Therapists. Saunders, St. Louis. 2009
Whittaker J L. Ultrasound Imaging for Rehabilitation of the Lumbopelvic Region: A Clinical Approach. Churchill Livingstone, Philadelphia, 2007.
Whittaker JL, Teyhen DS, Elliott JM et al. Rehabilitative ultrasound imaging: understanding the technology and its applications. J Orthop Sports Med 2007; 37(8): 434-449