## Slide 1: PTP 565
Fundamental Tests and Measures
Thomas Ruediger, PT, DSc, OCS, ECS
Statistics Overview

## Slide 2: Outline
Statistic(s)
Central Tendency
Distribution
Standard Error
Referencing
Sources of Errors
Reliability
Validity
  Sensitivity/Specificity
  Likelihood Ratios
Receiver Operator Characteristics (ROC) Curves
Clinical Utility

## Slide 3: Statistic(s)
A statistic
  “Single numerical value or index…”
  Rothstein and Echternach
Index
  a number or ratio (a value on a scale of measurement) derived from a series of observed facts
  wordnet.princeton.edu/perl/webwn
Descriptive or inferential?
  D: What we did and what we saw
  I: This is what you should expect in general population
Examples
  61.5 kg, 0.75, 0.25, 3.91 GPA ie. numbers and ratios

## Slide 4: Central Tendency
What is an average?
  Mean?
    μ for population
    X for sample
  Median?
  Mode?
Which do we use for each of these?
  Distribution of Names=mode (nominal-counting)
  Distribution of Ages=it depends
  Distribution of Gender=mode (nominal-counting)
  Distribution of Body Mass
  Distribution of Strength
How is it calculated?
  Sum/n
  Middle # (or middle two/2)
  Most frequent value

## Slide 5: Bell Curve
68.2% +/- 1 SD
95.4% +/- 2SD
99.7% +/- 3SD
Mu=mean of population

## Slide 6: Variability Population
How measurements differ from each other
  Measured from the mean
In total these difference always sum to zero
Variance handles this
  Sum of squared deviations
  Divided by the number of measurements
  σ2 for population variance
Standard deviation
  Square root of variance
  σ for population SD

## Slide 7: Variability (of the Sample, not Population)
How measurements differ from each other
  Measured from the mean
In total, these always sum to zero
Variance handles this
  Sum of squared deviations
  Divided by (the number of measurements – 1)
  s2 for sample variance (now a estimate_
  Also called an “unbiased estimate of the parameter σ2 “
    P & W p 396
Standard deviation
  Square root of variance
  s for sample standard deviation

## Slide 8: Calculating Variance and SD
1,3,5,7,9
5-1=4^2=16
5-9=4^2=16
5-3=2^2=4
5-7=2^2=4
16+16+4+4= 40/5=8
Variance: 8^2=64
SD: sqroot(64)= 8

## Slide 9: Skewed distributions

## Slide 10: Skewed distributions
Mean “pulled” to the tail by extreme measurements

## Slide 11: Mode=15 Median=15.26 Mean=15.6
These data from a reference values study, show a more subtle positive skew of the data..
The display is shown in a “binned” histogram - ……..

## Slide 12
Skewness
The amount of asymmetry of the distribution
Kurtosis
The peakedness of the distribution

## Slide 13: Standard error of the measure (SEM)
Product of the standard deviation of the data set and the square root of 1 - ICC
  SD x squroot of 1 - ICC
An indication of the precision of the score
Standard Error used to construct a confidence interval (CI) around a single measurement within which the true score is estimated to lie
95% CI around the observed score would be: Observed score ± 1.96*SEM
  Nearly 2SD but not quite (observed score +/- 2SD)
Weir JP. Quantifying test-retest reliability using the intraclass correlation coefficient and the SEM. J Strength Cond Res. Feb 2005;19(1):231-240.

## Slide 14: Minimum detectable difference (MDD)?
SEM doesn’t take into account the variability of a second measure
SEM is therefore not adequate to compare paired values for change
Of course there is a way to handle this
(1.96*SEM*√2)
Weir JP. Quantifying test-retest reliability using the intraclass correlation coefficient and the SEM. J Strength Cond Res. Feb 2005;19(1):231-240.
Eliasziw M, Young SL, Woodbury MG, Fryday-Field K. Statistical methodology for the concurrent assessment of interrater and intrarater reliability: using goniometric measurements as an example. Phys Ther. Aug 1994;74(8):777-788.

## Slide 15: Standard error of the mean (S.E. mean)
An estimate of the standard deviation of the population
An indication of the sampling error
Three points relative to the sample
  The sample is a representation of the larger population
  The larger the sample , the smaller the error
  If we take multiple samples, the distribution of the sample means looks like a bell shaped curve
Standard deviation / √ of the sample size (s/√n)
Equation 18.1 P & W

## Slide 16: Normative Reference
How does this datum compare to others?
Gives you a comparison to the group
Datum should be compared to similar group
  55 stroke patient vs. 25 year old athlete? WRONG
  25 year old soccer player vs. 25 year old swimmer? CORRECT!
Datum may (or may not) indicate capability
  Strength is +3 SD of normal
  Can he bench 200 kg?

## Slide 17: Criterion Reference
How does this datum compare to a standard?
For example, in many graduate courses
  All could earn an “A”
  All could fail
In contrast, Vs. Norm Referencing
  Same group above, but in norm referenced course
  Some would be “A”, some “B”, some “C”….
Criterion references often used in PT for
  Progression
  Discharge

## Slide 18: Percentiles
100 equal parts
Relative position
  89th percentile
  89% below this
Quartiles a common grouping
  25th (Q1), 50th (Q2), 75th (Q3) , 100th (Q4)
  Interquartile Range
    Distance between Q3-Q1
    Middle 50%
  Semi-interquartile Range
    Half the interquartile range
    Useful variability measure for skewed distributions

## Slide 19: Stanines
STAndard NINE
Nine-point
Results are ranked lowest to highest
Lowest 4% is stanine 1, highest 4% is stanine 9
Calculating Stanines
4% 7% 12% 17% 20% 17% 12% 7% 4%
1 2 3 4 5 6 7 8 9

## Slide 20: Sources of Measurement Error
Systematic: ruler is 1 inch too short for true foot
Random: usually cancels out
Individual
  Trained
  Untrained
The instrument
  Right instrument
  Same instrument
Variability of the characteristic
  Time of day
  Pre or post therapy

## Slide 21: Reliability
Test-Retest
  Attempt to control variation
  Testing effects
  Carryover effects
Intra-rater
  Can I (or you) get the same result two different times?
Inter-rater
  Can two testers obtain the same measurement?
Required to have validity

## Slide 22: Reliability
ICC reflects both correlation and agreement
  What PT use commonly
Kappa:
Others

## Slide 23: Validity
Not required for Reliability
Measurement measures what is intended to be measured
Is not something an instrument has=it has to be valid for measuring “something”
Is specific to the intended use
Multiple types
  Face
  Content
  Criterion-referenced
    Concurrent
    Predictive
  Construct

## Slide 24
Sensitivity and Specificity are components of validity

## Slide 25: Sensitivity
The true positive rate
Sensitivity
  Can the test find it if it’s there?
Sensitivity increases as:
  More with a condition correctly classified
  Fewer with the condition are missed
Highly sensitive test good for ruling out disorder
  If the result is Negative
  SnNout
1-sensitivity = false negative rate
EX: All people are females in classes is high sensitivity, but males are all then “false positives”

## Slide 26: Specificity
The true negative rate
Specificity
  Can the test miss it if it isn’t there?
Specificity increases as:
  More without a condition correctly classified
  Fewer are falsely classified as having condition
Highly specific test good for ruling in disorder
  If the result is positive
  SpPin
1-specificity = false positive rate

## Slide 27: Likelihood Ratios
Useful for confidence in our diagnosis
Importance ↑ as they move away from 1
1 is useless: means false negatives = false positives 50%
  Negative 0 to 1 Positive 1 to infinity
LR + = true positive rate/false positive rate
LR - = false negative rate/ true negative rate

## Slide 28
Truth
Test
+
+
-
Sp
Sn
a
b
c
d
NPV = d/c+d
PPV = a/a+b
1-Sn = - LR
+ LR = 1-Sp
Sp = d/b+d
Sn = a/a+c

## Slide 29: Receiver Operating Characteristics (ROC) Curves
Tradeoff between missing cases and over diagnosing
Tradeoff between signal and noise
Well demonstrated graphically
In the next slide you see the attempt to maximize the area under the curve
P & W have an example on page 637

## Slide 30: Receiver Operating Characteristics (ROC) Curves
Aka
Sensitivity
Aka
1 - specificity
Notes: WANT A POINT CLOSEST TO UPPER LEFT HAND CORNER

## Slide 31: Clinical Utility
Is the literature valid?
  Subjects
  Design
  Procedures
  Analysis
Meaningful Results
  Sn, Sp, Likelihood ratios
Do they apply to my patient?
  Similar to tested subjects?
  Reproducible in my clinic?
  Applicable?
  Will it change my treatment?
  Will it help my patient?

## Slide 32: Hypotheses
Directional
  I predict “A” intervention is better than “B” intervention
Non-directional
  I think there is a difference between “A” intervention and “B” intervention

## Slide 33: Evidence based practice
Ask clinically relevant and answerable questions
Search for answers
Appraise the evidence
Judge the validity, impact and applicability
Does it apply to this patient?
Sackett et al. Evidence-Based Medicine: How to Practice and teach EBM. 2nd ed.