## Slide 1: Wheelchairs and Evaluation of Patients for Wheelchairs, Bed Mobility and Documentation of ADL’s

## Slide 2: Final practical
UQ Screen/Lower Q Screen
Fit crutches
Using a cane/walker
Roll over in bed
One manual muscle tests (spinal/abdominal/STM)
ROM for cervical/thoracic/lumbar spine

## Slide 3: Objectives
Learn about the different wheelchair types
Break down a wheelchair into its parts
Measurement of a patient for a wheelchair
Risk Factors or what happens to the patient when the wheelchair doesn’t fit
Bed Mobility: what it is, how to evaluate for independence in bed mobility
Documentation for ADL’s including Gait and Posture

## Slide 4: Wheelchair Types
Standard Adult: < 250#
Heavy Duty Adult: >250# up to 600#
Intermediate/Junior: Adolescent 10-14
Growing: Frame is adjustable for growth but limited to a certain length
Child/Youth: up to age 6
Hemiplegic: lower seat for foot propulsion

## Slide 5: Standard Wheelchair
Basic Wheelchair
Found in hospitals, nursing homes etc.
No frills, chrome wheelchair
Durable, frequently non adjustable
Short term or infrequent use
Used in hospitals, airports, point A to Point B

## Slide 6: Heavy Duty Wheelchair
Will be covered by insurance if:
Patient weighs more than 200-250 lbs. then up to 600 lbs.
Reinforced back and seat

## Slide 7: Pediatric Considerations
Child/Youth
Allows a variety of positions
Caregiver height

## Slide 8: Specialized Types of Chairs
Amputee: axle is 2 inches behind the COG, wheels further back, anti-tippers
Indoor: Drive wheels are in the front

## Slide 9: Sports W/C
Sports:
low profile back,
light weight frame,
no arm rests,
foot bar,
narrow, angled wheels
-need to watch rubbing for the angled wheels

## Slide 10: Power Wheelchairs
Patients have UE impairments
Must have strength, coordination, ability to safely operate a wheelchair

## Slide 11: Reclining Wheelchairs
Tilt in Space
1. Gravity assist for trunk
balance
2. User who can’t maintain
an upright posture (for BP control)
3. Pressure Relief (ulcers)
4. Rear wheels are further back
5. Anti-tippers frequently installed (can be difficult, but safer)

## Slide 12: Stair Climbing Wheelchairs
Not covered by most insurances
FDA approved
Benefits Wheelchair uses in ability to go up and down steps, obstacles without assist
http://www.youtube.com/watch?v=ik286spRM1w

## Slide 13: Wheelchair Components

## Slide 14: Wheelchair Components
    Locks
      Toggle
      Caster

## Slide 15: Wheelchair Components
Wheels/Tires
  Casters and Drive Wheels:
    Rubber
    pneumatic
    semi-pneumatic
  Wheels Rims:
    spoke
    magnum
    Solid
  Depends on terrain

## Slide 16: Wheelchair Components
Hand rim
  Smooth
  Toggle-for hemi-palgic
  Projections
  Magnum is most common less spokes
  One arm drive: used for L and R steering on the side with the same good arm.

## Slide 17: Wheelchair Components
Leg Rests
  Fixed foot rest (sports)
  Swing Away/Removable (most desirable in general)
  Elevating (for amputees, diabetes)
Foot Rests
  Heel Loop
  Toe Loop
  Fixed
  Swing up
  Plates smooth or ridges

## Slide 18: Wheelchair Components
Arm Rests
  Fixed: standard w/c
  Desk/Cut-out: angled so can get close to desk.
  Removable: swing back or remove for transfers.
  Adjustable

## Slide 19: Wheelchair components
Back
  Solid
  Hammock/Sling
  Contoured
  Custom molded
  Semi to Full
  Lowe seat for sports.

## Slide 20: Wheelchair components
Seat
  Solid – removable or fixed
  Hammock/Sling

## Slide 21: Cushions:
Distribution of forces
  Weight of patient
  Shear forces
  Pressure distribution
  Heat dissipation
  Moisture tolerance
Many different types
  Silicone
  Gel: expensive, heavy, leak
  Foam: least expensive, doesn’t last long, and hard to clean.
  Air: maintenance, inflation
  Custom Molded

## Slide 22: Wheelchair Components
Restraints
  Lap Belt=helpful for safety, but get in the way, so they don’t wear them eventually and will sit on them.
  Chest Strap
  Butterfly Strap
  H Strap: like a backpack, most stable
  Padded Shoulder Straps

## Slide 23: Wheelchair Accessories
Lap Tray: hemiplegia so can rest hands
Arm Tray
O2 tank carrier
Baskets/Cloth Carriers

## Slide 24: Evaluating the Wheelchair Fit Seat Width
How to Measure
  Measure the widest part at level of greater trochanter
  Add 2 inches (one inch per side)
  Should be able to fit a hand on either side of thigh between thigh and wheelchair side surfaces.

## Slide 25: Seat Width, cont.
Too Wide
  Poor propulsion
  Door fit
  Allows for postural deviance
Too Narrow
  Skin irritation
  Inhibits transfer ease

## Slide 26: Evaluating the Wheelchair Fit Seat Length
How to Measure
  Measure lateral leg from posterior buttock to popliteal fold
  Subtract 2 inches (between 1 – 2 inches)
  Should be able to fit 2-3 fingers between seat and calf, need a space for back of knee.

## Slide 27: Seat Length, cont.
Too Long
  Skin breakdown at popliteal fossa
  Won’t allow 90o knee flexion
Too Short
  Skin irritation back of thigh
  Decreased back stability
  Increase weight to ischeal tuberosities

## Slide 28: Evaluating the Wheelchair Fit Seat Height
How to Measure
  Measure form heel to popliteal fold
  Add 2 inches (for footrest height)
  Feet should be 2 inches to clear the floor
  Hip/Knee angle should be 90o/90o

## Slide 29: Seat Height, cont.
Too High
  Poor propulsion
  Poor desk/surface fit
  Tipping forward risk
  Unable to touch floor with feet
Too Short
  Lowered footrests
  Increase hip angle
  Increase weight on the ischeal tuberosities

## Slide 30: Evaluating the Wheelchair Fit Armrest Height
How to Measure
  Measure from buttock to olecranon process with elbow held at 90o
  Add 1 inch plus seat cushion height if cushion is used
  From the posterior view, should see a triangle made up of backrest, humerus, and top of armrest with shoulders relaxed.

## Slide 31: Arm Rests, cont.
Too High
  Difficulty propelling chair
  Poor UE function/Poor transfers
  Postural deviations
Too Low
  Inadequate support/poor transfers
  Fatigue of trap lengthened
  Slump posture/abdominal discomfort

## Slide 32: Evaluating the Wheelchair Fit Back Height
How to Measure
  Measure from buttock on seat to bottom line of axillary fold
  Subtract 4 inches
  Should be able to fit 4 fingers between top of seat back and axilla

## Slide 33: Back Height, cont.
Too High
  Restricts scapular movement for UE fxn
  Skin irritation
Too Low
  May not give adequate trunk support

## Slide 34: Risk Factors for Pressure Areas
Dx (poor sensation, limited movements, pain meds)
Limited UE Function
Postural Deformities
Hours in chair
Types of Activities
Terrain: bumping, slides, rubbing
Climate: hot and sweaty.
Level of Independence
  Incontinence: uric acid causes skin breakdown
  Body build: at risk, bony, and overweight.
  Poor nutrition
  Excessive perspiration
  Sitting pressures and distribution of weight

## Slide 35: Bony weight bearing areas
Ischeal Tuberosities: # 1
Coccyx
Greater Trochanters: width of care
Spinous Processes: back of seat
Ears: head plate
Back of Head
Elbows
Knees
Ankles and Heels

## Slide 36: References
Batavia, M., The Wheelchair Evaluation a Practical Guide. Butterworth Heinemann,1998
Giannini, M. J., Choosing A Wheelchair System. Journal of Rehabilitation Research and Development Clinical Supplement #2, 1990.
Pierson, F. M., Principles & Techniques of Patient Care. 4th edition, Saunders Elsevier, 2008.

## Slide 37: Bed Mobility
Defined as the ability of a person to move about in bed
Includes such activities:
  rolling to either side
  scooting up in bed
  moving between supine and sitting
  both sitting and scooting on the edge of the bed

## Slide 38: Bed Mobility Progression
Stability precedes mobility
Maintaining a position precedes attaining a position
Static and dynamic stability with a large base of support precedes static and dynamic stability with a small base of support
Attaining a position with a low center of mass precedes attaining a position with a high center of mass

## Slide 39: Purpose of Bed Mobility Tasks
Encourages independence
Precedes transfers: rolling and sit up must happen first.
Helps patient avoid future problems
  soft tissue pressure
  development of contractures

## Slide 40: Bed Mobility Performed
Hook-Lying position: spine, bending knees up to chest.
Bridging
Scooting up in bed in supine position
Rolling: supine to sidelying
Supine to Prone
Supine to sit
Sit to supine
Sit to stand
Stand to sit

## Slide 41: Concerns
For Patients:
  Watch arms, hands
  Safety precautions for patients – lines, catheters
For Physical Therapists
  Body mechanics
  Assistance needed
  Don’t allow patient to hold you around the neck

## Slide 42: Documentation of Functional Activities

## Slide 43: Objectives:
Discuss Documentation of Posture, Balance, Gait
Define Assistance as it would be used in Documentation as per the Functional Independence Measure (FIM scores helps in placement into setting from acute)
Look at CPT codes for reimbursement
Define Assessment
  Problem List
  Goals

## Slide 44: Posture Documentation
Sitting
Standing
Supine
Prone
Posterior View, Anterior View, Lateral View
Type of Posture: give a name “scoliosis, flat-back”
Ability to correct poor posture “functional or structural”

## Slide 45: Types of Posture
Sagittal view: forward head posture, rounded anterior shoulders
Decreased Lumbar Lordosis
Increased Thoracic Kyphosis
Flat Back Posture

## Slide 46: Ex of Posture Documentation:
32 year old male with diagnosis of Scheurmann’s disease (wedging)
Posture: Sagittal view: patient exhibits a forward head, sharp angulated kyphosis between T3 and T7, flat lumbar spine with a posterior tilt of the innominates.

## Slide 47: Documentation of Bed Mobility, Balance, Gait and Wheelchair Use
Use of Functional Independence Measure (FIM) to determine the amount of assistance the patient utilizes for functional or bed mobility, balance, gait and wheelchair use.
CPT codes assist with amount of time spent on various functions associated with functional ability balance, gait and wheelchair use

## Slide 48: Functional Independence Measure (FIM)
Guide for the Uniform Data Set for Medical Rehabilitation (Adult FIM)
FIM(TM) is an 18-item ordinal scale, used with all diagnoses within a rehabilitation population.
It is viewed as most useful for assessment of progress during inpatient rehabilitation.

## Slide 49
FIM | Description | Documentation Form
Complete independence (FIM 7) | All tasks described as making up the activity are typically performed safely, without modification, assistive devices, or aids, and within reasonable time | Independent, I
Modified independence (FIM 6) | one or more of the following may be true: the activity requires an assistive device; the activity takes more than reasonable time, or there are safety (risk) considerations | Mod I

## Slide 50
FIM | Description | Documentation Form
Supervision or setup (FIM 5) | Subject requires no more help than standby, curing or coaxing, without physical contact, or, helper sets up needed items or applies orthoses | SBA
Minimal contact assistance (FIM 4) | Subject requires no more help than touching, and expends 75% or more of the effort | Min A
Contact guard | Variation of minimal assist where subject requires contact to maintain balance or dynamic stability | Don’t trust unless you are holding on to them.

## Slide 51
FIM | Description | Documentation Form
Moderate assistance (FIM 3) | Subject requires more help than touching, or expends half (50%) or more (up to 75%) of the effort | Mod A
Maximal assistance (FIM 2) | Subject expends less than 50% of the effort, but at least 25% | Max A
Total assistance (FIM 1) | subject expends less than 25% of the effort | TA

## Slide 52: Balance (NOT ON FINAL)
Type of test
Time
Norms (if known)
% deficit compared to norms

## Slide 53: Gait:
Type of assistance required:
  Supervised Assist SBA
    Not making contact with the patient, next to the pt “just in case”
  Minimal Assist
    Steadying the patient or need to touch the pt (like the old term of contact guard)
  Moderate Assist
  Maximal Assist

## Slide 54: Equipment Needed:
Cane
  Hemi cane
  Standard cane
  Quad cane
Walker
  Standard
  Rolling
  Platform
Crutches
  Axillary
  Forearm
  Platform

## Slide 55: Weight Bearing Status
NWB - Non weight bearing
TTWB – Toe touch weight bearing
  10% of weight
  Learn with toe touch, but begin normal gait pattern
PWB – Partial weight bearing
  50% of weight
WBAT or WBTT – Weight bear to tolerance
FWB – Full weight bearing
Document that the pt. was instructed in proper crutch use.

## Slide 56
Distance walked
Type of Surface: hard, carpeting, stairs, tile

## Slide 57: Gait pattern/deviations
Gait Deviations: no use of assistive device
  Muscle Weakness or Decreased Range
  Ex: Trendelenberg, Foot slap
Gait Pattern:
  Used with assistive devices
  Ex: 2-point, 3 point, 4 point gait

## Slide 58: Wheelchairs
Wheelchair management
  Assessment: document patient measurements
  Fitting: document type of wheelchair, measurements of wheelchair, patient fit within the wheelchair
  Training: document type of training the patient undergoes such as elevators, transfers, doors, falls etc.
  Document any problems, how the pt. fit, the standard steps, type of cushion, how to get in and out, up down on curb, etc

## Slide 59: Assessment
Professional judgment of PT
Identifies patient impairments, functional limitations and disabilities
Sets goals: long term (indepdent activity) and short term ( change in functional ability/disability) (2-4 visits, 2 weeks, day in acute)

## Slide 60: Problem List
Review of S and O portion of note
Only write down problem that can be changed or treated with PT, so look at the issue that can be fixed.
Determine which findings are abnormal and can be treated by physical therapy
Prioritize problems from most important to least important and list
Write goals based on problem list

## Slide 61: Goals
Short Term (completed with 3-4 visits)
Long Term Goals
Expected Functional Outcomes
Every problem should have a long term goal or expected functional outcome associated with it

## Slide 62: CPT Codes: Reimbursement Codes
CPT Codes | Description | 
97112 | Therapeutic procedure, one or more areas, each 15 minutes; neuromuscular reeducation of movement, balance, coordination, kinesthetic sense, posture and/or proprioception for sitting and/or standing activities. | Balance Posture
97116 | Therapeutic procedure, one or more areas, each 15 minutes; gait training (including stair climbing) | Include assessment and fitting of devices
97542 | Wheelchair management (assessment, fitting, training) each 15 minutes |