## Slide 1: Gait Deviations and Prosthetic Knee and Feet Systems
A Comprehensive Look at Prosthetic Knee and Foot Design and How it Affects Amputee Gait
Presented by: Bradley Shebib, MPT
Wright & Filippis

## Slide 2: Prosthetic Feet and Knees
Patient Evaluation
Amputation level
Activity level prior to amputation
Patient goals post amputation
Expected impact on prosthesis
Cosmetic concerns
Medicare functional levels
Insurance formularies

## Slide 3: Prosthetic Feet and Knees
Activity Levels
Evaluation of the patient’s lifestyle prior to amputation.
Return to pre-amputation function?
Patient goals and motivation post amputation.
Realistic expected outcomes.
Important to distinguish activity level from expected impact on the prosthesis.

## Slide 4: Prosthetic Feet and Knees
Additional Factors
Cosmetic concerns of the patient
Types of footwear preferred
Insurance concerns
Several highly functional and technologically advanced feet will not be approved by some insurance companies.

## Slide 5: Prosthetic Feet and Knees
Medicare Functional Levels
Implemented to define a patient’s potential functional level.
Adopted by private insurance companies as the standard measure of potential.
Levels 0 through 4
The patient’s functional level will govern the selection of the type of foot used.

## Slide 6: Prosthetic Feet and Knees
Medicare Functional Levels
Measurement of patient potential to accomplish his/her expected, post-rehabilitation, daily function.
K0 is not a prosthetic candidate

## Slide 7: Prosthetic Feet and Knees
Potential household ambulator
Walking from couch to bedroom
Potential limited community ambulator
Walking from house to neighbor’s house
Community ambulator with the potential for variable cadence
Working, walking, hiking
High activity user which exceeds normal ambulation skills
Running, sports
Very Low
Low
Moderate
High
K1
K2
K4
K3
Functional Levels/K Codes
Notes: <number>
K0: is a person that does not qualify for a prostetic, have to pay themselves
K levels are further classified into 4 major groups, ranging from K1(low functional level) to K4 (high functional level).
Notes:
K2: limited community ambulator, cant vary speeds, and only walk on one surface.
K3: vary speed, vary terrian,
K4: high level athletes, children that are running around.

## Slide 8: Prosthetic Feet and Knees
Pediatrics
Children are considered K4 patients due to their normal activities.
Notes: <number>
K levels are further classified into 4 major groups, ranging from K1(low functional level) to K4 (high functional level).
Notes:

## Slide 9: Prosthetic Feet and Knees
Bi-laterals
Bi-laterals are exempt from the Functional Level/K-Coding system due to the unique stresses upon their prostheses.
Most rehab professionals are unaware of this which leads to under-prescribing and continuous failures.
Notes: <number>
K levels are further classified into 4 major groups, ranging from K1(low functional level) to K4 (high functional level).
Notes:

## Slide 10: Prosthetic Feet
Prosthetic feet should provide the following functions:
Joint simulation
Shock absorption
A stable weight-bearing base of support
Muscle simulation
Cosmesis

## Slide 11: Prosthetic Feet
Prosthetic Feet Classifications
S.A.C.H: K1-2, low level can’t do BAPs board because can’t compile to uneven surface.
Single Axis
Multi-Axial
Energy Storing
Some prosthetic feet incorporate a combination of classifications.
Notes: 40-60% more work
<number>

## Slide 12: Prosthetic Feet
S.A.C.H.
(Solid Ankle Cushioned Heel)
Consists of a solid wood or aluminum internal keel extending to the toe break
The keel is surrounded by a molded external foam foot with cosmetic toes and a cushioned heel wedge.
No moveable parts.
Plantar flexion is replaced by the compression of the heel wedge.
Shock absorption at heel strike is very good.
SACH feet provide excellent stability.
Historically fit to low active patients and used in post-operative prostheses.

## Slide 13: Prosthetic Feet
S.A.C.H.
(Solid Ankle Cushioned Heel)
Advantages: Moderate weight Good durability No moving components Minimal maintenance Good shock absorption for moderately active patients. | Disadvantages: Limited plantar flexion and dorsi-flexion adjustability. The heel cushion deteriorates over time. Heel cushion may loose elasticity Poor shock absorption for high active patients.

## Slide 14: Prosthetic Feet
S.A.C.H. – Gait Deviations
(Solid Ankle Cushioned Heel)
1. Soft heel cushion will create strong extension moment at the knee
2. Lack of strong toe lever limits how long stability is maintained through stance
3. Limited adaptability to different surfaces

## Slide 15: Prosthetic Feet
Single Axis Feet
Contains a solid wood internal keel, a molded foam rubber shell, a metal single axis joint, a rubber plantar flexion bumper, and a dorsiflexion stop.
Ankle plantar flexion and dorsiflexion are provided in the rotation about the ankle joint.
Offers shock absorption at heel strike through the plantar flexion bumper, which is available in multiple durometers.
Stance-phase stability is excellent because the foot in in contact with the ground for a long period of time

## Slide 16: Prosthetic Feet
Single Axis Feet
Advantages: The plantar flexion capability provides increased knee stability at heel strike and foot flat and may lessen the difficulty of descending inclines Plantar flexion resistance can be varied | Disadvantages: Relatively high maintenance due to moving components Increased weight Less cosmetic Tendency to “squeak”

## Slide 17: Prosthetic Feet
Single Axis Feet – Gait Deviations
1. Plantarflexion will create strong extension moment at the knee
2. Limited adaptability to variable surfaces
3. Lower energy return

## Slide 18: Prosthetic Feet
Flexible Keel Feet
Contains a keel made of a flexible material.
The compliant keel aids in shock absorption.
Multi-terrain uses
Water safe applications
Low cost

## Slide 19: Prosthetic Feet
Multi-Axial Feet
The multi-axial foot provides motion in all three planes, making it particularly suitable for patients who walk on uneven terrain.
1
2
3
4

## Slide 20: Prosthetic Feet
Multi-Axial Feet
Advantages: Allows motion is all planes Reduces torque on the residual limb Adjustability | Disadvantages: Increased weight Increased maintenance

## Slide 21: Prosthetic Feet
Energy Storing
Modern materials have made it possible for prosthetic feet to absorb, store, and release energy.

## Slide 22: Prosthetic Feet
Energy Storing
Advantages: Extremely light weight All activity levels can benefit Longer stride Less oxygen consumption Exceptional shock absorption Excellent cosmesis Individually customized | Disadvantages: Misconception that Energy Storing Feet are only appropriate for the high active patients Higher cost/reimbursement scale

## Slide 23: Prosthetic Feet
Multi-Axial, Energy Storing Feet – Gait Deviations
1. Higher adaptability to uneven surfaces
2. Depending on length of heel and toe lever, will see strong extension/flexion moment at the knee
3. Increased energy return leads to more dynamic gait

## Slide 24: Prosthetic Feet
Medicare Levels and Prosthetic Feet Options
Any SACH foot or Single Axis Foot
Any flexible keel foot or multi-axial foot

## Slide 25: Prosthetic Feet
Medicare Levels and Prosthetic Feet Options
A Flex foot system, energy storing foot, multiaxial ankle/foot, dynamic response or flex walk system

## Slide 26: Above Knee Categories
Joint Type
- Single Axis
- Polycentric Axis
Swing Control Mechanism
- Constant Friction
- Fluid Control
Stance Control Mechanism
- Manual Lock
- Friction Pad
- Fluid Control
Notes: <number>
Single Axis – 3R45, C-Leg, Mauck unit. Polycentric – Total Knee, 3R60. Constant Friction – low level knees = 3R49, 3R36, wt. activated stance. Fluid Control = C-Leg, Mauck, 3R60, any mod to high level knee. Manual Lock = 3R40. Friction pad – wt activated stance. Fluid control = c-leg, rheo knee.

## Slide 27: Friction vs Hydraulic Control
Constant Friction Knees
- LESS DYNAMIC SWING CONTROL SYSTEM
- Less speed variability due to friction control
- If High Friction:
1. will see more posterior pelvic tilt and hip thrust to fight resistance
2. Will see lower heel rise on prosthetic side
- If Low Friction:
1. will see more “flipping” of leg, rebounding from terminal extension before heel contact
2. Will see higher heel rise on prosthetic side

## Slide 28
Friction vs Hydraulic Control
Hydraulic Knees
- MORE DYNAMIC KNEE CONTROL SYSTEM
- Patient can expect greater speed variability
- IF HYDRAULICS TOO STIFF:
1. Pt will complain of “walking through mud”
2. Lower heel rise, more posterior tilt to fight through resistance
- IF HYDRAULICS TOO LOOSE:
1. Pt will experience excessive heel rise
2. Pt will aggressively extend knee, having difficulty controlling terminal knee extension

## Slide 29
Two Types of Swing Control
- Constant Friction
- Hydraulic/Pneumatic
Two Types of Forefoot Unloading
- Breaks the knee without un-weighting
- Must un-weight to get knee flexion
Medicare Functional Level – K2 or Below (with one exception)
Single Axis – Weight Activated Stance Control Knee

## Slide 30
Single Axis – Weight Activated Stance Control Knee
K1 or K2 | K1, K2 OR K3
K1 or K2 | NONE
Constant Friction
Hydraulic/Pneumatic
Forefoot Unloading
No Forefoot Unloading
Notes: <number>
All have an extension assist in the form of an external or internal spring.

## Slide 31
Single Axis – Weight Activated Stance Control Knee
- MAKE SURE to have patient weight shift to prosthetic side to secure loading of weight activated brake. This is true of all W.A.S. systems!!
- Tendency to “sit back” on sound side, wait for prosthesis to hit ground. LESS SAFE WITH THIS SYSTEM
Notes: <number>
All have an extension assist in the form of an external or internal spring.

## Slide 32
Constant Friction/No Forefoot Load
- MOST LIMITED OF W.A.S. KNEES
- Hip Hike needed to unweight the prosthesis
- Tendency to circumduct prosthetic side
- Inconsistent knee extension moment due to no geometric lock
- Tendency to “sit back” on sound side, wait for prosthesis to hit ground. LESS SAFE WITH THIS SYSTEM
- Increased time on sound side noted
Single Axis – W.A.S.
Expected Gait Deviations

## Slide 33
Constant Friction/Forefoot Loading
- No Hip hike needed to unweight prosthesis
- Less circumduction during swing phase
- Increased time on prosthetic side which reduces stress on sound side
Single Axis – W.A.S.
Expected Gait Deviations
Notes: <number>
Patient will have the tendency to “sit back” with swing of the sound side because of creating the extension moment at the knee physically because they know the knee gives easily

## Slide 34
Hydraulic/Forefoot Loading
- NO hip hike needed due to forefoot loading
- Further reduction in circumduction
Single Axis – W.A.S.
Expected Gait Deviations

## Slide 35
Two Types of Swing Control
- Constant Friction
- Hydraulic/Pneumatic
Options with Stance Flexion Feature
- Some have stance flexion through bumper system from heel contact to midstance
Medicare Functional Levels
- K2 or below for friction knees
- K3 or above for hydraulic/pneumatic knees
Polycentric Knees

## Slide 36
Polycentric Knees
K1 or K2 | K3 or above
K1 or K2 | K3 or above
Constant Friction
Hydraulic/Pneumatic
Stance Flexion
No Stance Flexion

## Slide 37
Polycentric Knees – Expected Gait Deviations
Delayed gait to wait for sound of terminal knee
extension – common with all polycentric knees
“flipping” of knee – using distal end of residual
limb to disengage stance lock and swing the leg
Powerful hip extension moment at heel contact
to ensure locking of knee through midstance
PATIENT NEEDS mild hip flexion “pop” to
overcome geometric lock of knee system
Notes: <number>
Talk to your prosthetist about adjusting the friction setting to meet the patients’ individual needs. These are the safest knees – K2 level patients, least amount of variability seen.

## Slide 38
Constant Friction
- DEPENDING ON FRICTION SETTING – will either see excessive heel rise, toe drag, or excessive hip flexion moment to overcome resistance.
- AT HIGHER SPEEDS – you will notice a firm terminal impact, causing delayed heel contact
- AT LOWER SPEEDS – you will notice difficulty reaching terminal impact prior to heel contact
- MAKE SURE FRICTION ADJUSTMENT IS APPROPRIATE FOR INDIVIDUAL PATIENT
Polycentric Knees – Expected Gait Deviations
Notes: <number>
Talk to your prosthetist about adjusting the friction setting to meet the patients’ individual needs. These are the safest knees – K2 level patients, least amount of variability seen.

## Slide 39
Constant Friction/No Stance Flexion
- More “pole vaulting” due to lack of stance flexion feature
- More “thumping” of sound side as patient comes down off of prosthetic limb
- Slowest patient speed expected, most patient fatigue throughout training session
Polycentric Knees – Expected Gait Deviations

## Slide 40
Constant Friction/Stance Flexion
- Less “pole vaulting” due to stance flexion feature
- Less “thumping” of sound side as patient is able to maintain smoother center of gravity through midstance
- Higher patient speed expected, decreased patient fatigue throughout training session due to more controlled gait pattern
Polycentric Knees – Expected Gait Deviations

## Slide 41
Hydraulic/No Stance Flexion
- “pole vaulting” over prosthetic side due to no stance flexion
Hydraulic/Stance Flexion Knees
- less “pole vaulting” needed if patient allows stance flexion to occur
Polycentric Knees – Expected Gait Deviations
Notes: <number>
As with constant friction knees, hydraulic resistance will play into heel rise, toe drag and overall cadence of gait.

## Slide 42
Wide Variety of Knee Systems
- Examples – C-Leg, Mauch, Rheo Knee
Medicare Functional Level
- All K3 or Above
Single Axis – Hydraulic/Pneumatic

## Slide 43
Hydraulic/Pneumatic Resistance Influences Gait Expectations
- IF TOO STIFF – fluid drag will cause pt to increase hip hike/flexion to propel prosthesis. Pt feels like they are “dragging through mud”
- IF TOO LOOSE – decreased stance time on prosthetic side due to lack of overall confidence, feeling of knee instability
Single Axis, Hydraulic/Pneumatic – Expected Gait Deviations

## Slide 44
Hydraulic/Pneumatic Resistance Influences Gait Expectations
- IF TOO STIFF – may see lack of heel rise, powerful “flip” of prosthesis to propel leg.
- IF TOO LOOSE – May see excessive heel rise, difficulty reaching terminal impact at heel contact, thus slowing gait down to allow leg to catch up.
Single Axis, Hydraulic/Pneumatic – Expected Gait Deviations

## Slide 45
Ability to disengage hydraulics increases activity variability
- Mauck, C-Leg, Rheo will “shut off” hydraulics if patient achieves hyperextension moment at toe off. Allows for easier swing of knee.
- If no hyperextension, pt will “ride” the hydraulics, increasing energy expenditure through swing phase.
Single Axis, Hydraulic/Pneumatic – Expected Gait Deviations

## Slide 46
Ability to engage stance control increases patient confidence
- Otto Bock 3R80 is free swinging unless weight is put on leg, then hydraulic resistance kicks in for controlled knee flexion.
- Different from W.A.S. as weight doesn’t lock prosthesis, only offers more controlled movement.
Single Axis, Hydraulic/Pneumatic – Expected Gait Deviations

## Slide 47
How Can We As Physical Therapists Help Maximize Patient Outcomes With Their Respective Knee Systems?

## Slide 48
Know the knee system prior to starting treatment
Talk to the prosthetist about any adjustments made prior to starting treatment
Monitor patient gait deviations and ask that adjustments be made as the patient progresses
Tailor your expectations to each individual knee system
Maximizing Patient Outcomes

## Slide 49
QUESTIONS???