## Slide 1: Supplemental Oxygen & Ventilators

## Slide 2: Supplemental Oxygen Delivery
Signs & Symptoms: CO2 Retention/Acidosis
  Altered Mental Status
    Lethargy
    Drowsiness
  Headache
  Tachycardia & Diaphoresis
  Tremor
  Blueish of Skin and sclera
  HTN

## Slide 3: FIO2
Fraction of inspired oxygen
Expressed as a number from 0 (0%) to 1 (100%)
FiO2 of normal room air is 0.21 (21%)

## Slide 4: Supplemental Oxygen Delivery
Types of Supplemental O2 Delivery
  Variable Performance FIO2
  Fixed FIO2
FIO2 Determination
  Tidal Volume
  Respiratory Rate
  Type fit and placement of the Mask
  May be different at rest vs. activity

## Slide 5: Oxygen Masks

## Slide 6: COPD pts. use low flow oxygen to:
Relieve dyspnea
Promote  functional capacity
 exercise endurance
Allow pt. to exercise at a higher HR
Reach training threshold
 minute ventilation
Improve oxygen delivery to exercising ms.
 OBLA
 brochoconstriction

## Slide 7: Supplemental Oxygen Delivery
Examples of FIO2 with a nasal cannula
  1 L/min = 24% FIO2
  2 LPM = 28% FIO2
  3 LPM = 32% FIO2
  6 LPM = 44% FIO2

## Slide 8: Supplemental Oxygen Delivery
Nasal Cannula
  1-6 L/min
  Skin breakdown
  Tubing limits mobility
  Tripping over tubing
Nasopharyngeal Catheter
  Tubing inserted to uvula/held with tape
  Humidified
  Pediatric patients

## Slide 9: Supplemental Oxygen Delivery
Open Face Mask
  35-50% FIO2
  Humidified
Closed Face Mask
  5-8 L/min
  50-60% FIO2
  Difficult to cough, talk, eat; very drying

## Slide 10: Supplemental Oxygen Delivery
Trans-tracheal Catheter
  Surgically inserted
  Hygienic Maintenance
Tracheostomy Mask or collar
  FIO2 25-70%
  Difficult talking, eating
  Drying

## Slide 11: Supplemental Oxygen Delivery
Partial Non-rebreather Mask
  35-95% FIO2
  Highest [O2]
  Limited PT
  Hygiene issues

## Slide 12: Supplemental Oxygen Delivery
Air Entrainment Mask; Venti or Venturi Mask
  Provides specific fixed FIO2
  Talking, coughing, eating issues

## Slide 13: Supplemental Oxygen Delivery
CPAP Mask
  Continuous Positive Airway Pressure
  Used for Sleep Apnea
  Use of room air
  Considerations:
    Comfort
    Bruising under straps
    Dries tissues

## Slide 14: Supplemental Oxygen Delivery
BiPAP
  FIO2 =21-100%
    Positive Inspiratory/end expiratory pressures
    May avoid intubation and mechanical ventilation
    Used at home for sleep apnea
    Noisy, claustrophobic, facial abrasions

## Slide 15: Supplemental Oxygen Delivery
T- tube/piece
  Specific O2 to intubated spontaneously breathing patient during weaning
  Attached directly to trach
  Humidified
  Clinical Tip:
    Consult physician and nursing for PT during weaning
    Pt may be anxious and medicated

## Slide 16: Pulmonary Challenges
Mechanical Ventilator
  Hypoxemia
  Ventilatory Failure
  Airway Adjuncts
  A: Endotrach
  B: Nasotrach
  C: Endotrach with cuff
  D: Trach with cuff

## Slide 17: Airways/Intubation
Nasotracheal or Endotracheal Intubation

## Slide 18: Mechanical Ventilation
Positive pressure to inflate lungs
  Promote pulmonary gas exchange
  Increase lung volume
  Reduce work of breathing
Indications
  Pa O2 < 50 mm Hg. With O2
  bpm < 10 L/ min
  Inspiratory force < 2.5 cm H2O
  Protect airway from gastric aspiration
  Reversal of Respiratory muscle fatigue

## Slide 19: Mechanical Ventilation
Settings
  Oxygenation
    FIO2
    Positive End-Expiratory Pressure (PEEP)
  Ventilation
    RR & VT
    Inspiratory Flow Rate
    Inspiratory to Expiratory Ratio
    Pressure Sensitivity; hyperventation & mm fatigue

## Slide 20: Mechanical Ventilation
Positive pressure ventilators
  Halt Inhalation and allow Exhalation by
    Pressure Cycling
    Volume Cycling
    Time Cycling

## Slide 21
VT = Tidal volume measured in the first min in the T piece trial NIF=Neg Inspir Force

## Slide 22: Mechanical Ventilation
Control Ventilation (CV):
  Total Control
Assisted Control (AV):
  Pt controls RR and pattern; used with weak breathing
Assist/Control:
  either as needed
Synchronous Intermittent-Mandatory Ventilation (SIMV)
  Like AV but preset RR VT and flow

## Slide 23: Mechanical Ventilation
Pressure Supported:
  Constant Inspiratory pressure
Continuous Positive Airway Pressure
  Pressure delivered in both inspiration & Exhalation

## Slide 24: Mechanical Ventilation
Problems
  11 days of total ventilator support
    25 % loss of diaphragm strength
    36% loss of diaphragm endurance
  Barotrauma
    Pressure damages lung tissue
  Oxygen Toxicity
    Dries and damages tissues
  Reduces respiratory drive
  Reduces Cardiac Output

## Slide 25: Mechanical Ventilation
Weaning Criteria
  Spontaneous Breathing
  RR < 35
  Inspiratory Force > 20 cm H2O
  FIO2 < 50 %
  SaO2 > 90%
  RR/VT ratio > 105

## Slide 26: Alarms
Oxygen Failure
  Bag the patient
Pressure
  Obstructions
  Worsening medical condition
  Low pressure usually indicate a leak in the system
Volume
  Measures minute ventilation and or tidal volume
  Low volume may be from a deflated cuff or pt spontaneously breathes
  High volume from increased RR due to agitation, activity

## Slide 27: Alarms and Trach
Remain calm
Replace the trach tube onto the trach
Follow back to the ventilator